Project4 :pedestrian detection
------------------------------------------------------------------------------------------------------------------------
Step 1
Import the required libraries of python OpenCV ,nump and imutilus .Numpy is used for easy matrix operations.imultius is a series of convenience functions to make basic image processing functions such as translation, rotation, resizing, skeletonization, and displaying Matplotlib images easier with OpenCV.

import numpy as np
from imutils.object_detection import non_max_suppression
from imutils import paths
import cv2

------------------------------------------------------------------------------------------------------------------------
 Step 2
   `	capture the frames for image processing in one of the method given below

1. cap = cv2.VideoCapture('test/video4.mp4') --> from video file
2. cap = cv2.VideoCapture(0) --> from camera

Note : Here ‘0’ indicates the primary cmera of your computer .We can choose the desired camera by its numer in here.

------------------------------------------------------------------------------------------------------------------------
 Step 3

initialize the HOG descriptor/person detector

hog = cv2.HOGDescriptor()
hog.setSVMDetector(cv2.HOGDescriptor_getDefaultPeopleDetector())

------------------------------------------------------------------------------------------------------------------------
Step 4
 Here we read the image and convert it to grayscale. Many operations in OpenCV are done in grayscale.

ret, frame = cap.read()

1.ret : True-> for sucessfull capture
False- >for faled capture
2.frame:The image frame
------------------------------------------------------------------------------------------------------------------------
Step 5
Rescale the input imgae for fast perfomance

   image = cv2.resize(image, None, fx=ds_factor, fy=ds_factor, interpolation=cv2.INTER_AREA)

------------------------------------------------------------------------------------------------------------------------

------------------------------------------------------------------------------------------------------------------------Step 6

detect people in the image frame using hog detection

rects,weights=hog.detectMultiScale(image,winStride=(4,4),padding=(8,8),scale=1.05)

------------------------------------------------------------------------------------------------------------------------
Step 7

Draw a rectangle box in each detected people

    for (x,y,w,h) in rects:
        cv2.rectangle(orig,(x,y),(x+w,y+h),(0,0,255),2)

- Orig:Input image
- (x,y) : Vertex of the rectangle.
- (x+w,y+h) : Vertex of the rectangle opposite to pt1 .
- (0,0,255) :Rectangle color or brightness (grayscale image).
- 2:Thickness of lines that make up the rectangle. Negative values, like CV_FILLED , mean that the function has to draw a filled rectangle.

apply non-maxima suppression to the bounding boxes

    rects = np.array([[x, y, x + w, y + h] for (x, y, w, h) in rects])
pick = non_max_suppression(rects, probs=None, overlapThresh=0.65)

# draw the final bounding boxes
for (xA, yA, xB, yB) in pick:
cv2.rectangle(image, (xA, yA), (xB, yB), (0, 255, 0), 2)

------------------------------------------------------------------------------------------------------------------------
Step 8
 Next is to display the ouput frame.

    cv2.imshow('output', frame)

This is a cv2 function used to display the image. It also takes two arguments: the first one is the name of the window that will pop-up to show the picture and the second one is the image you want to display.
------------------------------------------------------------------------------------------------------------------------

------------------------------------------------------------------------------------------------------------------------Step 9

To escape from while loop we use a key interrupt,Once the ‘esc’ is pressed the the loop get break.ASCII value of esc is 27 in decimal and OpenCV wait for a cycle for keypress.

    if cv2.waitKey(1) == 27:
        break
------------------------------------------------------------------------------------------------------------------------
Step 10

De-allocate any associated memory or device usage.

cap.release()	->This will relase the camera allocated for our project.
cv2.destroyAllWindows()	->This simply destroys all the windows we created using	cv2.imshow(window_name, image)
------------------------------------------------------------------------------------------------------------------------